## Slide 1: Steps in ESR Setup
78Kr
72Ge
Be 1cm
target
slits
inject 78Kr into ESR at g ~ gt
measure gt with electron cooler (isochronicity curve)
inject 78Kr through target, measure target thickness
set ESR to Br of isochronous 72Ge, optimize injection
new ESIS for 72Ge at same Br after target
Check resolution with frequency lines of same A/Z = 2.25
ESR fine tuning, cut Br distribution with scrapers

## Slide 2: Setting Details
LISE file of beamline
and ESR acceptance
gt = 1.41, E/m = 381.9 MeV/u => BrESR (72Ge) = 6.9401 Tm
Target 1850 mg/cm2 Be => ESIS = 453.9 MeV/u
Low transmission (~ 0.2 %)
only 380 72Ge / 109 Kr
Expected fragments
in order of intensity:
74As, 72Ge, 69Ga, 67Zn, 76Se, 70Ga, 77Br, 65Cu, 62Ni, 60Co, .. , 68Zn, …

## Slide 3: ESR Isochronous Mode
gt is not constant depends on orbit in ESR
DBr/Br [10-3]
= df/f
transform by calculation to other m/q or g
„Cooler curve“ as test of isochronicity
Scan beam Br with electron cooler